Open Source Power Supply

Technical Requirement Specification

Use of a Laptop / readily available Power Suppl

- Voltage and current adjstable
  - Voltage can be set with a resolution of 10mV
  - Current limit can be set with a resolution of 10mA
  - Voltage can be varied between 0V and power supply input to OSPS
  - How do we stop power supply providing current out of spec of the input supply? Ask the user to en sure in the spec? watch for voltage drop when overcurrent?
Low BoM Cost – use of CoTs enclosure
- Electronics will be contained in an enclosure on which dials/displays can be mounted
  - Variant 1 – CoTs enclosure adapted by during assembly
  - Variant 2 – 3D printed enclosure
 USB Type C – if we have time, it would be good to put this support in