Part number	Cost	Integration approach	Advantages	Disadvantages	Image
NUCLEO-F042K6	£7.99 (Farnell)	- USB socket is for debug only / -Sockets placed on PCB so entire dev board can be integrated in to OSPS	- No need for MCU PCB design / - Nice dev environment for STM32 / - Inexpensive / - Can upgrade by removing dev board from socket	- No USB interface / - Have to add cost of sockets to BoM
NUCLEO-F302R8	£6.48 (Farnell)	- USB socket is for debug only / - Debug section removed from board to service as ST programmer / - MCU de-soldered from board and soldered down on OSPS board so / MCU can then be programmed in-situ	- USB interface possible / - Inexpensive / - User has a programmer to upgrade MCU when required / - Nice dev environment for STM32	- User must de-solder LQFP package / - Documentation required for hacking programme
MSP-EXP430G2	£7.63 (Farnell)	- Micro held in socket on dev board so program on board and place in socket on OSPS	- Simple transfer to design	- Micro not very sophisticated / - No USB comms
Arduino ISP	£9.39 (RS)	- A cheap programmer for use with all atmel micros	- Simple	- Expensive as mirco brought separately / - Arduino dev environment is rubbish
RasPi B+	£20.75 (Farnell)	- Fit to socket on OSPS	- Lots of computing power / - Simple USB connection / - Linux	- No analogue inputs / - Expensive
Sainsmart UNO	£9.99 (amazon)	- Rip off arduino / - Program on device on dev board an move over to socket on OSPS	- Simple	- No USB connection / - Arduino dev environment is rubbish